## Slide 1: Autonomous Gas Leak Detection In Distilleries Using A Mobile Robotic Sensor Platform
BSc Computer Science (Artificial Intelligence) - Aadham Ahmad
Supervised by Dr. Alistair McConnell

## Slide 2: Problem & Motivation
Gas leaks in distilleries are dangerous
  Ethanol => flammable
  Methane => explosive
  CO₂ => asphyxiation risk
Current monitoring is limited:
  Fixed sensors => poor spatial coverage
  Manual inspection => slow & unsafe
Problem: Monitoring is reactive, not proactive

## Slide 3: Aim & Contributions
Develop an autonomous system to detect and localise gas leaks
Key Contributions for proposed mobile robotic platform including:
    Sensor payload using low-cost sensors
    Lightweight embedded firmware
    Gas distribution mapping (GDM)
    Gas source localisation (GSL)

## Slide 4: System Overview

## Slide 5: Hardware Setup
Robotic Platform
TurtleBot3 (LiDAR-based SLAM)
Sensor Payload
MOX gas sensors (BME690)
Wind sensors (air velocity)
Particulate sensor (SPS30)
Processing
ESP32 (sensor interface)
Jetson Nano (proposed onboard computation)

## Slide 6: Gas Distribution Mapping (GDM)
Goal: Estimate gas concentration across space
Robot collects:
  Gas readings
  Position
  Wind data
Builds a 2D gas map

## Slide 7: Gas Source Localisation (GSL)
GSL using PMFS strategy

## Slide 8: Comparative Evaluation of GSL Methods
Evaluated 6 GSL Methods:
Probabilistic Methods: PMFS, GrGSL
Reactive Methods: Spiral, Surge-Cast, Surge-Spiral, Particle Filter
Convergence Time for GSL Methods
Error Distance for GSL Methods

## Slide 9: Limitations & Future Work
Limitations
  Simulation-based evaluation
  2D modelling of gas flow
  Sensor noise & delay
Future Work
  Real-world deployment
  3D gas modelling
  Improved sensor fusion

## Slide 10: Conclusion
Developed an autonomous gas detection system
Demonstrated GDM + GSL
Shows potential for safer industrial monitoring